THE YIELD STRESS ON WET FOAM

Dhineshkumar Balasubramaniam
Immatrk. No : 21971603
dhineshpsgmech@gmail.com

Abstract – Most of the common foams are two-phase medium of gas and liquid with a particular structure consisting of gas pockets trapped in a network of thin liquid films and plateau borders. When Foams have high yield stress, they are useful in fluid for carrying particles in applications ranging from the transport of cuttings in drilling and the placement of sands in cracks in oil producing reservoirs to increase the conductivity of reservoirs for secondary oil recovery. The rheology of wet foam gives the yield stress behavior but the behavior of the wet foam is difficult due to its complex structure and nature of the components. In 19th century, Joseph Plateau clearly described that, Wet foam is an example of soft matter with a very well defined structure.

Index Terms – Wet foams, Rheology, Plateau border, yield stress, surfactants.

# INTRODUCTION

Foams are playing major roles in particles transporting like froth flotation, oil movement and so on. It is important to develop a constitutive rheological law, predicting the relation between macroscopic stress, strain and strain history. Foams exhibit linear viscoelastic behavior when they are subjected to small shear stresses and flow like viscous liquids when the shear stress is large enough to trigger bubble rearrangements. Foam elasticity comes from the deformation of bubbles from the perfectly sphere shape, in order to increase their packing density. During deformation, the stored surface energy is increased and this is responsible for viscoelastic properties of foam.

A well-developed science of dry, static (or quasi-static) foams is a valuable first step. Most common foams are quite dry when in equilibrium under gravity, and we can understand most of their properties when they are in this condition. These include the essential structure, as Plateau described it long ago, the statistics associated with that structure, its coarsening with time due to gas diffusion, its elastic and plastic properties, and the drainage of liquid through it when equilibrium is disturbed. In order to understand the behavior of wet foam, we have been using successful theories of dry foam, based on the assumption that fluid is mainly within the Plateau borders.
# How Foams are formed?
## Foam formation
Most of the common foams are a two-phase medium of gas and liquid with a particular structure consisting of gas pockets trapped in a network of thin liquid films and plateau borders. Some well known foams are bubble baths, dishwater

detergents and the foam head on beers. Many oils foam when trapped gas is suddenly released under conditions of an abrupt
drop in pressure. In some refiners in which the through-flow of gas at high temperature and pressure is required to crack hydrocarbons, the gas-liquid mixtures will foam strongly. The foam traps gas with gas fractions of 80% or higher. Clearly in such situations, in which it is desired that solid catalysts contact liquids, the production of foam is not wanted.

In other applications, foams are useful; for example foams which have a high yield stress and can be used in a fluid for carrying particles in applications ranging from the transport of cuttings in drilling and the placement of sands in cracks in oil producing reservoirs to increase the conductivity of reservoirs for secondary oil recovery. Obviously, bubble bath and shampoo companies should like to produce appropriate foams for dish and hair washing. Technologies which are impacted by foams and foaming are widespread.
## Plateau's law
Plateau's laws describe the shape and configuration of soap films as follows:
1. Soap films are made of entire (unbroken) smooth surfaces.
2. The mean curvature of a portion of a soap film is everywhere constant on any point on the same piece of soap film.
3. Soap films always meet in threes along an edge called a Plateau border, and they do so at an angle of arccos(−1/2) = 120°.
These Plateau borders meet in fours at a vertex, and they do so at an angle of arccos(−1/3) ≈ 109.47° (the tetrahedral angle).

Fig. 1. Bubbles in a foam of soapy water obey Plateau's laws. (left) All Plateau surfaces intersect three by three in 120 degrees angle. (right) At every vertex the angle is close to 109.47 degrees, the tetrahedral angle.
## Plateau Border
Plateau defines the border in foam, Where films meet along a line or curve, there is a liquid-filled interstitial channel. Plateau used the concept of a geometrical (fully dry or ideal) foam consisting of films of negligible thickness that are joined along lines and at points. Films are endowed with a free energy %gamma per unit area, which, if the film thickness is negligible, coincides with the film tension %sigma , leading to the total foam energy E_{ 0 } = %gamma S where S is the total film area.

Figure 4: The elements of a foam, illustrating Plateau’s laws. In the dry limit, (a) three films meet in a single Plateau border and (b) four Plateau borders meet in a single junction. This junction is formed at the meeting point of six films in a tetrahedral-shaped wire frame, such as Plateau used to discover the laws which bear his name. When liquid is added to a foam, the Plateau borders (c) and junctions (d) become swollen, meeting the films with a zero contact angle.
# Stability of Wet foams / Liquid foams
Stability factors
The physical properties of a foam depend on its liquid fraction, Φ i.e. the volume ratio of liquid and gas. Dry foams refer to Φ less than about 0.05 (as generally holds for detergent foams), wet foams refer to Φ higher than about 0.15 (as in freshly poured beer). Values of liquid fraction higher than 0.36 correspond to bubbly liquids. In equilibrium under gravity, most common foams are quite dry.

Figure 4: Foam structures can be computed using the Suface Evolver software (Brakke, 1992). The examples shown here are the Waire-Phelan structure for Φ = 0 and Kelvin cells for Φ = 0.01 and Φ = 0.10.

Generally wet foams are only stable if they contain surfactants. Their most important effect is not simply that of lowering the surface tension, although it is closely related. Rather, it is the dynamical properties of the surface tension which serve to stabilize the films. The surface tension increases whenever a film is suddenly stretched locally, resulting in increased forces which oppose that tendency.

The other factor which makes foam more stable is dis-joining pressure. This expresses mutually repulsive force between the two faces of films, which makes foam film more thinning. The film thickness at equilibrium is achieved by determining the balance between dis-joining pressure and the bulk pressure of liquid. Latter decreases to large negative values as the liquid fraction of the foam decreases,and the Plateau borders shrink and increase in curvature.

Foam drainage
Whenever there is a finite amount of liquid in the foam, it is subject to gravity-driven drainage, unless it has already come into equilibrium under gravity. In this state, there is a vertical profile of liquid fraction. This is related to a variation of the local pressure in the liquid according to the hydrostatic pressure law, necessary for equilibrium under gravity.

Figure 8: (a) The forced-drainage experiment, in which a solitary wave is observed to descend through the foam, has greatly improved our understanding of liquid drainage through foams. In this case the position of the wave-front was measured using conductivity. (b) The numerical solution of a foam drainage equation allows us to verify the agreement between theory and experiment.

More generally, the liquid moves through the Plateau borders and junctions of the static foam structure (and to a lesser extent the films) in response to gravity and local pressure variations. An understanding of this process, particularly in the limit of low liquid fraction, has been aided by the development of nonlinear foam drainage equations. The most striking example of drainage is the solitary wave-front which propagates down through the foam when liquid is added to the top at constant flow-rate. See figure 8. This is known as a forced drainage experiment. The velocity of the front is constant to a good approximation, and easily observed. This simple measurement is a good starting point in exploring drainage, and its dependence on the nature of surfactants (Saint-Jalmes and Langevin 2002).

Stress – strain behavior
Foam is a complex fluid and it exploits various material properties under different strain rates. It behaves like elastic solids at low strain, behaves like plastic solids when strain increases and like liquid at very high strain.

Figure 9: In an experiment in which the strain is slowly increased, the stress first increases linearly. The slope is the elastic shear modulus. This increase continues until the plastic limit, at which the first topological changes occur and the foam yields. The system shows hysteresis in the sense that once the foam has yielded, the stress drops to a lower limit stress characterized by further intermittent topological changes and liquid-like behavior (flow). In practice, the difference between the limit stress and the yield stress is small, and both depend significantly upon the strain-rate.

The yield stress of a Foam
The life history of an liquid foam neglects one important aspect of liquid foam; their mechanical properties, which are remarkable, considering that the constituents of the foam (a gas and a dilute surfactants solution) behave individually as unexceptional and quite predictable fluids. A foam can flow like a liquid or remain motionless under stress like a solid. For example shaving cream lather is easy to spread, it offers little resistance to flow and gives the impression of having a low viscosity. Yet the stress due to gravity is not enough to cause shaving cream lather to flow in the hand or when it has been spread; the manifestation of what seems to be low viscosity depends on whether a parameter called yield stress has been exceeded.

The physical basis for the yield stress of a foam can be explained by a simple model in which a foam is treated as a two-dimensional honeycomb of hexagonal cells. When the cells are all the same size, the model satisfies the Plateau criteria for a real foam. Suppose the foam is subjected to a shearing force, its deformation under that force is straightforward as long as the volume of each cell can stay constant and films can continue to meet in threes at angles of 120 degrees. Then a critical strain is reached, when the cells are so deformed that some of the Plateau border have coalesced and the films between them have disappeared.

Four films now meet at each junction and its violating the rules of stability. In this unstable configuration the foam has been forced to generate an energetically unfavourable amount of surface area. The structure of the foam thus makes a sudden transition to a new strtucture resembling the original honeycomb except that the cells are rearranged and some cells that originally were in contact have separated. This rearrangement constitutes the flow of the foam. In addition it defines the yield stress. The yield stress is the amount of force per unit area that triggers a deformation in which cells jump past one another to take up new positions. For dry films the yield stress turns out to the size of the cells. Latter finding should be no surprise: fine-celled shaving cream lather is much stiffer than coarse-celled laundry soapsuds.

The bubble dynamics simulation method
In this task, we use a 3D extension to Durian’s original bubble dynamics model to study the rheology of wet polydisperse foams. This extension requires special handling of the repulsive forces between bubbles in 3D, and necessitates the calculation of a stress tensor from velocities and positions of single bubbles. The next section introduces the computational methodology, and is followed by a description and discussion of steady shear results.

In detail, the bubble dynamics model assumes that inertial effects on bubble motion are insignificant in comparison to the effects of inter-bubble compression forces and dissipation in the thin films separating moving bubbles. Therefore at every time-step, the sum of forces on the ith bubble is zero,

        vec {F}^drag _{ i }+ vec {F}^neigh_{ i } = vec{ 0 }	(1)

force on bubble ith due to to shearing in thin films, by relative motion between neighboring bubbles, is approximated by
        vec {F}^drag_{ i } = {- C %eta_{ w} langle R rangle ^2 } over {%delta} sum from{j} ( vec{v}_{i} - vec{v}_{j} ) = -b.n_{ i }( vec{v}_{i} - langle vec{v}_{j} rangle ) (2)

where the total area of a bubble covered by thin films is A_{ t } = C langle R rangle^2 , and b =A_{ t } %eta_{ w }/%delta In Eq. (2), v_{ j } is used to represent the average velocity of neighboring bubbles.

In Eq. (1), vec {F}^neigh_{ i } represents the total force on bubble i due to compression from contacting neighboring bubbles and is determined by summing the pairwise forces F_{ ij } between all bubble pairs in the simulation system within each time step. The form of the force between contacting bubbles will be discussed in more detail later. For now, it is readily seen that the substitution of Eq. (2) in Eq. (1) yields an equation of motion for each bubble,

vec{v}_{i} = langle vec{v}_{j} rangle + {1} over {b.n_{i}} sum from{j=1 , j<>1} to{N} { vec{F}_{ij} } (3)

Note that when n_{i }=0,vec{F}_{ ij }=0 and vec{ v }_{ i } = langle vec{ v }_{ j } rangle . The liquid in the thin films is assumed to display Newtonian behavior. The restoring (repulsive) force due to a single compression surface is found to be,

vec{F}_{%xi i} = {12.%pi R_{ i }F_{ o }c_{ i }( n_{i} ) %alpha_{ i }( n_{i} )} over { langle R rangle } left [ left ( {1} over {1- %xi_{i}}right)^3 - 1 right]^{%alpha_{ i }(n_{i})-1} { 1 } over ({1- %xi_{i}})^4 { vec{r}_{i}-vec{r}_{i} } over abs { vec{r}_{i}-vec{r}_{i} } (4)

where %xi_{ i } is the non-dimensional bubble compression, and F_{ o } = %sigma langle R rangle .The constants c_{ i }( n_{i} ) and %alpha _ { i }( n_{i} ) are functions of n_{ i } , the number of compressing surfaces or contacting neighbors on bubble i, and are listed in Table (1).

Configuration of contacting surfaces	n_{ i }	c_{ i }( n_{i} )	%alpha _ { i }( n_{i} )
Parallel plates	2	0.007	2.1
Two pair of perpendicular plates	4	0.012	2.1
Tetrahedron	4	0.014	2.1
Cube	6	0.021	2.2
Octahedron	8	0.027	2.3
Rhombic dodecahedron	12	0.055	2.5
Pentagonal dodecahedron	12	0.054	2.5
Icosahedron	20	0.069	2.6

Table 1 . Empirical contacting neighbor number dependent constants obtained by Lacasse et al. and used to evaluate the bubble interaction force in Eq. (4)

The total compression between an overlapping bubble pair is simply the sum of compressions of each bubble, that is

(R _ { i } + R_{j})%xi_{ij} = R _ { i } %xi_{i} + R_{j}%xi_{i}	(5)

and where,
%xi_{ij} = {R _ { i } + R_{j} - abs { vec{r}_{i} - vec{r}_{j} }} over {R _ { i } + R_{j} }	(6)

If the interacting bubble pair is treated as springs in series, the interaction force may be determined from ,

vec{F} _ { ij } = vec{F} _ { %xi i } = -vec{F} _ { %xi j } (7)

The calculation of %xi_{ i } and %xi_{ j } from Eqs. (4)–(7) is not straightforward, as it needs to be done numerically for each neighbor pair at each time step. We found that these rigorous calculations are very time consuming. Therefore, in keeping with the spirit of the simple bubble dynamics simulations in 2D, in this paper we use a more efficient and simpler process for evaluating vec{F}_{ ij } , than the solution of Eqs. (4)–(7). The force between bubbles i and j is simply approximated as

vec{F}_{ij} = {6.%pi (R_{ i }+R_{j})F_{ o }c_{ av } %alpha_{ av }} over { langle R rangle } left [ left ( {1} over {1- %xi_{ij}}right)^3 - 1 right]^{%alpha_{ av }-1} { 1 } over ({1- %xi_{ij}})^4 { vec{r}_{i}-vec{r}_{i} } over abs { vec{r}_{i}-vec{r}_{i} } (8)

where %alpha_{ av } and c_{ av } are the average value of these parameters between the i and j bubble pair, that is ,

%alpha_{ av } = 0.5[ %alpha_i (n_i)+ %alpha_j(n_j) ] and c_{ av } = 0.5[ c_i (n_i)+ c_j(n_j) ]
# Conclusion
A conclusion section is not required. Although a conclusion may review the main points of the paper, do not replicate the abstract as the conclusion. A conclusion might elaborate on the importance of the work or suggest applications and extensions.
Appendix
Appendixes, if needed, appear before the acknowledgment. This is an unnumbered section.
Acknowledgment
The preferred spelling of the word “acknowledgment” in American English is without an “e” after the “g.” Use the singular heading even if you have many acknowledgments. Avoid expressions such as “One of us (S.B.A.) would like to thank ... .” Instead, write “F. A. Author thanks ... .” Sponsor and financial support acknowledgments are placed here. This is an unnumbered section.
References
1. G. O. Young, “Synthetic structure of industrial plastics (Book style with paper title and editor),”	in Plastics, 2nd ed. vol. 3, J. Peters, Ed. New York: McGraw-Hill, 1964, pp. 15–64.
2. W.-K. Chen, Linear Networks and Systems (Book style).	Belmont, CA: Wadsworth, 1993, pp. 123–135.
3. H. Poor, An Introduction to Signal Detection and Estimation. New York: Springer-Verlag, 1985, ch. 4.
4. B. Smith, “An approach to graphs of linear forms (Unpublished work style),” unpublished.
5. E. H. Miller, “A note on reflector arrays (Periodical style—Accepted for publication),” IEEE Trans. Antennas Propagat., to be published.
6. J. Wang, “Fundamentals of erbium-doped fiber amplifiers arrays (Periodical style—Submitted for publication),” IEEE J. Quantum Electron., submitted for publication.
7. C. J. Kaufman, Rocky Mountain Research Lab., Boulder, CO, private communication, May 1995.
8. Y. Yorozu, M. Hirano, K. Oka, and Y. Tagawa, “Electron spectroscopy studies on magneto-optical media and plastic substrate interfaces (Translation Journals style),” IEEE Transl. J. Magn.Jpn., vol. 2, Aug. 1987, pp. 740–741 [Dig. 9th Annu. Conf. Magnetics Japan, 1982, p. 301].
9. M. Young, The Techincal Writers Handbook. Mill Valley, CA: University Science, 1989.
10. J. U. Duncombe, “Infrared navigation—Part I: An assessment of feasibility (Periodical style),” IEEE Trans. Electron Devices, vol. ED-11, pp. 34–39, Jan. 1959.
11. S. Chen, B. Mulgrew, and P. M. Grant, “A clustering technique for digital communications channel equalization using radial basis function networks,” IEEE Trans. Neural Networks, vol. 4, pp. 570–578, Jul. 1993.
12. R. W. Lucky, “Automatic equalization for digital communication,” Bell Syst. Tech. J., vol. 44, no. 4, pp. 547–588, Apr. 1965.
13. S. P. Bingulac, “On the compatibility of adaptive controllers (Published Conference Proceedings style),” in Proc. 4th Annu. Allerton Conf. Circuits and Systems Theory, New York, 1994, pp. 8–16.
14. G. R. Faulhaber, “Design of service systems with priority reservation,” in Conf. Rec. 1995 IEEE Int. Conf. Communications, pp. 3–8.
15. W. D. Doyle, “Magnetization reversal in films with biaxial anisotropy,” in 1987 Proc. INTERMAG Conf., pp. 2.2-1–2.2-6.
16. G. W. Juette and L. E. Zeffanella, “Radio noise currents n short sections on bundle conductors (Presented Conference Paper style),” presented at the IEEE Summer power Meeting, Dallas, TX, Jun. 22–27, 1990, Paper 90 SM 690-0 PWRS.
17. J. G. Kreifeldt, “An analysis of surface-detected EMG as an amplitude-modulated noise,” presented at the 1989 Int. Conf. Medicine and Biological Engineering, Chicago, IL.
18. J. Williams, “Narrow-band analyzer (Thesis or Dissertation style),” Ph.D. dissertation, Dept. Elect. Eng., Harvard Univ., Cambridge, MA, 1993.
19. N. Kawasaki, “Parametric study of thermal and chemical nonequilibrium nozzle flow,” M.S. thesis, Dept. Electron. Eng., Osaka Univ., Osaka, Japan, 1993.
20. J. P. Wilkinson, “Nonlinear resonant circuit devices (Patent style),” U.S. Patent 3 624 12, July 16, 1990.
21. IEEE Criteria for Class IE Electric Systems (Standards style), IEEE Standard 308, 1969.
22. Letter Symbols for Quantities, ANSI Standard Y10.5-1968.
23. R. E. Haskell and C. T. Case, “Transient signal propagation in lossless isotropic plasmas (Report style),” USAF Cambridge Res. Lab., Cambridge, MA Rep. ARCRL-66-234 (II), 1994, vol. 2.
24. E. E. Reber, R. L. Michell, and C. J. Carter, “Oxygen absorption in the Earth’s atmosphere,” Aerospace Corp., Los Angeles, CA, Tech. Rep. TR-0200 (420-46)-3, Nov. 1988.
25. (Handbook style) Transmission Systems for Communications, 3rd ed., Western Electric Co., Winston-Salem, NC, 1985, pp. 44–60.
26. Motorola Semiconductor Data Manual, Motorola Semiconductor Products Inc., Phoenix, AZ, 1989.
27. (Basic Book/Monograph Online Sources) J. K. Author. (year, month, day). Title (edition) [Type of medium]. Volume (issue).	Available: http://www.(URL)
28. J. Jones. (1991, May 10). Networks (2nd ed.) [Online]. Available: http://www.atm.com
29. (Journal Online Sources style) K. Author. (year, month). Title. Journal [Type of medium]. Volume(issue), paging if given.	Available: http://www.(URL)
30. R. J. Vidmar. (1992, August). On the use of atmospheric plasmas as electromagnetic reflectors. IEEE Trans. Plasma Sci. [Online]. 21(3). pp. 876–880. Available: http://www.halcyon.com/pub/journals/21ps03-vidmar