THE YIELD STRESS ON WET FOAM

Dhineshkumar Balasubramaniam (21971603)

Abstract

Most of the common foams are two-phase medium of gas and liquid with a particular structure consisting of gas pockets trapped in a network of thin liquid films and plateau borders. When Foams have high yield stress, they are useful in a fluid for carrying particles in applications ranging from the transport of cuttings in drilling and the placement of sands in cracks in oil producing reservoirs to increase the conductivity of reservoirs for secondary oil recovery. The rheology of wet foam gives the yield stress behavior but the behavior of the wet foam is difficult due to its complex structure and nature of the components. In 19th century, Joseph Plateau clearly described that, Wet foam is an example of soft matter with a very well defined structure.

Introduction

Foams are playing major roles in particles transporting like froth flotation, oil movement and so on. It is important to develop a constitutive rheological law, predicting the relation between macroscopic stress, strain and strain history. Foams exhibit linear viscoelastic behavior when they are subjected to small shear stresses and flow like viscous liquids when the shear stress is large enough to trigger bubble rearrangements. Foam elasticity comes from the deformation of bubbles from the perfectly sphere shape, in order to increase their packing density. During deformation, the stored surface energy is increased and this is responsible for viscoelastic properties of foam.

In order to fully characterize the foam with theoretical descriptions, we have to know the bubble diameter, liquid volume fraction and the solution surface tension . And its necessary to understand how yielding depends on the foam components. In order to understand the behavior of wet foam, we have been using successful theories of dry foam, based on the assumption that fluid is mainly within the Plateau borders.

How Foams are formed?

Most of the common foams are a two-phase medium of gas and liquid with a particular structure consisting of gas pockets trapped in a network of thin liquid films and plateau borders. Some well known foams are bubble baths, dishwater detergents and the foam head on beers. Many oils foam when trapped gas is suddenly released under conditions of an abrupt drop in pressure. In some refiners in which the through-flow of gas at high temperature and pressure is required to crack hydrocarbons, the gas-liquid mixtures will foam strongly. The foam traps gas with gas fractions of 80% or higher. Clearly in such situations, in which it is desired that solid catalysts contact liquids, the production of foam is not wanted.

In other applications, foams are useful; for example foams which have a high yield stress and can be used in a fluid for carrying particles in applications ranging from the transport of cuttings in drilling and the placement of sands in cracks in oil producing reservoirs to increase the conductivity of reservoirs for secondary oil recovery. Obviously, bubble bath and shampoo companies should like to produce appropriate foams for dish and hair washing. Technologies which are impacted by foams and foaming are widespread.

Plateau's law

Plateau's laws describe the shape and configuration of soap films as follows:
1. Soap films are made of entire (unbroken) smooth surfaces.
2. The mean curvature of a portion of a soap film is everywhere constant on any point on the same piece of soap film.
3. Soap films always meet in threes along an edge called a Plateau border, and they do so at an angle of arccos(−1/2) = 120°.
4. These Plateau borders meet in fours at a vertex, and they do so at an angle of arccos(−1/3) ≈ 109.47° (the tetrahedral angle).

Plateau Border

Plateau used the concept of a geometrical (fully dry or ideal) foam consisting of films of negligible thickness that are joined along lines and at points. Films are endowed with a free energy %gamma per unit area, which, if the film thickness is negligible, coincides with the film tension %sigma , leading to the total foam energy E_{ 0 } = %gamma S where S is the total film area.

Geometry of Foam

Foams are composed of gas and a small volume of liquid that separates the bubbles. A useful geometric idealization is to consider the foam composed of identical tetrahedral bubbles along with its surrounding channels and nodes.